## Slide 1: ELE427 COMMUNICATION THEORY – II
ANKARA UNIVERSITY
FACULTY OF ENGINEERING
ELECTRICAL AND ELECTRONICS ENGINEERING DEPARTMENT

## Slide 2: ELE427 COMMUNICATION THEORY - II
LECTURE 13
ERROR CONTROL CODING:
DECODING OF CONVOLUTIONAL CODES (VITERBI ALGORITHM)

## Slide 3
Decoding Methods
There are three generic methods for decoding convolutional codes.
At one extreme, the Viterbi algorithm executes maximum-likelihood decoding and achieves optimum performance but requires extensive hardware for computation and storage.
At the other extreme, feedback decoding sacrifices performance in exchange for simplified hardware.

## Slide 4
Decoding Methods
Between these extremes, sequential decoding approaches optimum performance to a degree that depends upon the decoder’s complexity.
We’ll describe how these methods work with a (2, 1, L) code.
The extension to other codes is conceptually straightforward, but becomes messy to portray for k>1.

## Slide 5
Decoding Methods
Recall that a maximum-likelihood decoder must examine an entire received sequence Y and find a valid path that has the smallest Hamming distance from Y.
However, there are possible paths for an arbitrary message sequence of N bits, so an exhaustive comparison of Y with all valid paths would be an absurd task in the usual case of N 1.

## Slide 6
Decoding Methods
The Viterbi algorithm applies maximumlikelihood principles to limit the comparison to surviving paths, independent of N, thereby bringing maximum-likelihood decoding into the realm of feasibility.

## Slide 7
Decoding Methods
A Viterbi decoder assigns to each branch of each surviving path a metric that equals its Hamming distance from the corresponding branch of Y.
Summing the branch metrics yields the path metric, and Y is finally decoded as the surviving path with the smallest metric.
To illustrate the metric calculations and explain how surviving paths are selected, we’ll walk through an example of Viterbi decoding.

## Slide 8
Decoding Methods
Suppose that our (2, 1, 2) encoder is used at the transmitter, and the received sequence starts with Y=11 01 11.
Figure 13.3–10 (Carlson, page 629) shows the first three branches of the valid paths emanating from the initial node a0 in the code trellis.

## Slide 9
Decoding Methods
The number in parentheses beneath each branch is the branch metric, obtained by counting the differences between the encoded bits and the corresponding bits in Y.
The circled number at the right-hand end of each branch is the running path metric, obtained by summing branch metrics from a0.

## Slide 10
Decoding Methods
Now observe that another path also arrives at node b3 and has a smaller metric 2 +1 + 0 = 3.
Regardless of what happens subsequently, this path will have a smaller Hamming distance from Y than the other path arriving at b3 and is therefore more likely to represent the actual transmitted sequence.

## Slide 11
Decoding Methods
Figure 13.3–11 (Carlson, page 630) depicts the continuation of Fig. 13.3–10 (Carlson, page 629) for a complete message of N 12 bits, including tail 0s.
All discarded branches and all labels except the running path metrics have been omitted for the sake of clarity.

## Slide 12
Decoding Methods
A Viterbi decoder must calculate two metrics for each node and store surviving paths, each consisting of N branches.
Hence, decoding complexity increases exponentially with L and linearly with N.
The exponential factor limits practical application of the Viterbi algorithm to codes with small values of L.

## Slide 13: References
Communication Systems, An Introduction to Signal and Noise in Electrical Communication, 5th edition, A.B. Carlson, P.B. Crilly, J.C. Rutledge, Mc Graw Hill.
An Introduction to Analog and Digital Communications, 2nd edition, S. Haykin, M. Moher, Wiley.