## Slide 1: ELE427 COMMUNICATION THEORY – II
ANKARA UNIVERSITY
FACULTY OF ENGINEERING
ELECTRICAL AND ELECTRONICS ENGINEERING DEPARTMENT

## Slide 2: ELE427 COMMUNICATION THEORY - II
LECTURE 14
ERROR CONTROL CODING:
TURBO CODING AND DECODING

## Slide 3
Turbo Codes
Turbo codes, or parallel concatenated codes (PCC), are a relatively new class of convolutional codes first introduced in 1993.
They have enabled channel capacities to nearly reach the Shannon limit.
Detailed treatments of turbo codes are given by Berrou, Glavieux, and Thitmajshima (1993), Berrou and Glavieux (1996), Hagenauer, Offer, and Papke (1996), Benedetto, al Montorsi (1996) and Johannesson and Zigangirov (1999).

## Slide 4
Turbo Codes
Shannon’s theorem for channel capacity assumes random coding with the bit error rate (BER) approaching zero as the code’s block or constraint length approaches infinity.
It is therefore not feasible to decode a completely truly random code. Increases in code complexity accomplished by longer block or constraint lengths require a corresponding exponential increase in decoding complexity.

## Slide 5
Turbo Codes
Turbo codes overcome this paradox in that they can be made sufficiently random to achieve a given BER and, by using iterative methods, can be efficiently and feasibly decoded.

## Slide 6
Turbo Codes
Figure 13.3–16 (Carlson, page 636) illustrates a turbo encoder.
Here we have the parallel concatenation of two codes produced from two rate recursive systematic convolutional (RSC) encoders.

## Slide 7
Turbo Codes
The second RSC is preceded by a pseudo-random interleaver whose length can vary from 100–10,000 bits or more to permute the symbol sequence.
The RSCs are not necessarily identical, nor do they have to be convolutional, and more than two can be used. Both encoders produce the parity-check bits.

## Slide 8
Turbo Codes
These parity bits and the original bit stream (called the systematic bits) are multiplexed and then transmitted. As given, the overall rate is 1/3.
However, we may be able to increase this rate to R=1/2 using a process of puncturing, whereby some bits are deleted.
This could be done, for example, by eliminating the odd parity bits from the first RSC and the even parity bits from the second RSC.

## Slide 9
Turbo Codes
Figure 13.3–17 (Carlson, page 636) shows a G1, G2-RSC encoder that has been used for turbo coding.
Unlike the nonsystematic convolutional (NSC) encoders described earlier in this section, this encoder is systematic in that the message and parity bits are separate.

## Slide 10
Turbo Codes
The turbo decoder is shown in Fig. 13.3–18(Carlson, page 637).
It consists of two maximum a posterior (MAP) decoders and a feedback path that works in similar manner to that of an automobile turbo engine, hence the term turbo code.

## Slide 11
Turbo Codes
The first decoder takes the information from the received signal and calculates the a posteriori probability (APP) value.
This value is then used as the a priori probability value for the second decoder.
The output is then fed back to the first decoder where the process repeats in an iterative fashion with each iteration producing more refined estimates.

## Slide 12
Turbo Codes
Instead of using the Viterbi algorithm, which minimizes the error for the entire sequence, this MAP decoder uses a modified form of the BCJR (Bahl, Cocke, Jelinek, and Raviv, 1972) algorithm that takes into account the recursive character of the RSC codes and computes a log-likelihood ratio to estimate the APP for each bit.

## Slide 13
Turbo Codes
The main disadvantage of turbo codes with their relatively large codewords and iterative decoding process is their long latency.
A system with 65,537 interleaving and 18 iterations may have too long a latency for voice telephony.
On the other hand, turbo codes have excellent performance in deep space applications.

## Slide 14: References
Communication Systems, An Introduction to Signal and Noise in Electrical Communication, 5th edition, A.B. Carlson, P.B. Crilly, J.C. Rutledge, Mc Graw Hill.
An Introduction to Analog and Digital Communications, 2nd edition, S. Haykin, M. Moher, Wiley.