## Slide 1: Polymer Technology
Chapter 5
Chemical Bonding and Polymer Structure

## Slide 2: Chemical Bonding and Polymer Structure
It is aimed to illustrate how the unusual properties of high macromolecules are developed.
In order to do this, it will be convenient to take into account the chemical and structural aspects of polymers at three different levels:
1. The chemical structure or atomic composition of the monomer or primary structure
2. The single polymer chain, which is the secondary level
3. The aggregation of polymer chains, which is the tertiary structure
In order to understand the polymer structure, it is needed to consider the molecular forces effective in polymers.

## Slide 3: Chemical Bonding
The electronic structure of atoms will determine the type of bond between the atoms concerned.
The chemical bonds need to be classified as primary or secondary depending on the extent of electron involvement.
The outermost electrons, which are valence electrons, are involved in the formation of the primary bonds.
The bond formation results in a substantial lowering of the potential energies.
Hence, the primary bonds are quite strong compared to the secondary bonds.
In contrast to the primary bonds, valence electrons are not involved in the formation of secondary bonds, which leads to weak bonds compared to the primary bonds.

## Slide 4: Chemical Bonding
Primary and secondary bonds can be categorized into the following subgroups:
1. Primary bonds
a. Ionic
b. Covalent
c. Metallic
2. Secondary bonds
a. Dipole
b. Hydrogen
c. Induction
d. van der Waals (dispersion)

## Slide 5: Chemical Bonding
The inert gases have completely filled s and p outermost orbitals, which results in a spherical distribution of electrons around the nuclei of the inert gases.
The inertness of these gases means that their electronic configuration provides stability.
All elements except inert gases seek to achieve this stable inert gas electronic configuration.
Elements apart from inert gases do this by either losing, gaining, or sharing electrons.
In order to attain the inert gas electronic configuration, the elements, losing electrons and the elements, gaining electrons, lead to the ionic bond.
Sodium chloride (NaCl) is well-known exampke for ionic bond.
Sodium can easily lose the outermost 3s electron to achieve the stable inert gas configuration and chlorine can gain an extra eletron to achieve a stable electronic configuration.

## Slide 6: Chemical Bonding
If the sodium atom loses an electron, it results in a positively charged sodium ion.
If the chlorine atom gains an extra electron, it results in a negatively charged chloride ion.
The electrostatic attraction between the two ions, the sodium ion and the chlorine ion, results in the bonding force in sodium chloride.
The central elements of the periodic table can not form ionic bonds since a large amount of energy is required to ionize the valence electrons.
On the other hand, the desired stable electronic configuration can be attained by the sharing of valence electrons.
In this case, the bonds formed by electron sharing are called covalent bonds.
If we consider the methane molecule, the carbon atom has four unpaired electrons in its outer electron shell and the hydrogen atom has one electron.

## Slide 7: Chemical Bonding
Although molecules are electrically neutral, they will have a permanent dipole if the centers of the positive and negative charges do not coincide.
It can be illustrated on HCl molecule, which is a diatomic molecule.
The chlorine atom within the molecule is more electronegative compared to the hydrogen atom.
Hence, the shared pair of electrons between the chlorine atom and the hydrogen atom is drawn closer to the chlorine atom, which means that the chlorine atom has net negative charge and the hydrogen atom has a net positive charge as show below.

## Slide 8: Chemical Bonding
The diatomic molecule, which has a separation of positive and negative charge, can be said to be polar.
In molecules with more than two atoms, the polarity of the molecule can be determined by the bond angles between the atoms.
The polar molecules have a small separation of charge, which results in a permanent dipole.
The polar molecules are held together in the solid state by the interaction among the charges on the molecules.
This interaction among the charges is opposed by thermal agitation, which means that the dipole–dipole interaction is temperature dependent.
The dipole forces play a significant role in the resulting tertiary structure.

## Slide 9: Chemical Bonding
A special type of dipole interactions is the hydrogen bond.
The bond between the hydrogen atom and the small electronegative atom such as florine, oxygen, or nitrogen leads to the stated hydrogen bond.
Water is a well-kown example for the hydrogen bond.
The difference in electronegativity values of hydrogen atom and oxygen atom results in the bonding electrons in H2O to shift to the oxygen atom.
Hence, the hydrogen atom behaves almost as bare proton.
Hydrogen bonding is limited to the molecules including florine, nitrogene, and oxygen since the small size of hydrogen atom permits the specified atoms to approach the hydrogen atom in another molecule very closely.

## Slide 10: Chemical Bonding
Each dipole creates an electric field associated with it.
The specified electric field is able to induce relative displacements of the electrons and nuclei in neighboring molecules.
Hence, the surrounding molecules around the molecue with the dipole become polarized, which is known as the induced dipole.
An intermolecular force, which is also known as the induction force, exist between the permanent and the induced dipole.
The specified induction force is weak and temperature independent.
Electrons of each atom are usually in constant motion about their nuclei.
Thus, the center of negative charge of the electrons cloud may not coincide with those of the nuclei and an instantaneous dipole may exist even in nonpolar materials.

## Slide 11: Chemical Bonding
The inert gases can not form any type of bonds such as ionic bond, covalent bond, or metallic bond.
At sufficiently low temperature, the inert gases can condense to form liquids.
The gases can also solidify at sufficiently low temperatures.
It means that some form of intermolecular force should exists within these materials.
The chemical properties and the electrical properties of a plastic material are directly related to the chemistry of the monomers, which constitute the specified plastic material.
On the other hand, the physical properties and the mechanical properties of a plastic material are largely a consequence of the macromolecular size of the plastic material.
As a definition, a macromolecule is a chain of atoms bonded together by primary valence bonds.

## Slide 12: References
Robert O. Ebewele, «POLYMER SCIENCE AND TECHNOLOGY», CRC Press, 2000.
Fried, Joel R., «Polymer science and technology», Prentice Hall, Third edition.