## Slide 1: COM332
Chapter 3: Transport Layer
(PART 1)

## Slide 2: Outline
Transport Layer Services
Connectionless Transport: UDP
Principles of Reliable Data Transfer

## Slide 3: Transport Layer Services
Transport layer provides logical communication between application processes
Transport protocols run in end systems
There are two transport layer protocols
  TCP
  UDP

## Slide 4: Transport Layer Services
TCP
  Reliable, in-order delivery
  Congestion control
  Flow control
  Connection setup
UDP
  Unreliable, unordered delivery
  No extension of best-effort IP
Delay guarantees and bandwidth guarantees arenat available on TCP and UDP

## Slide 5: Connectionless Transport: UDP
UDP
  Best effort service
  UDP segments may be lost, or delivered out of order to applicaiton
  Connectionless
  No handshaking between UDP sender and receiver
  UDP is used by:
    Streaming Multimedia
    DNS
    SNMP

## Slide 6: Connectionless Transport: UDP
Why UDP?
  No connection establishment (which can add delay)
  Simple: No connection state at sender or receiver
  Small header size
  No congestion control: (can blast away as fast as desired)

## Slide 7: Connectionless Transport: UDP
UDP Checksum
  Used to detect errors in transmitted segment
  Sender:
    Treat segment contents as a sequence of 16 bit integers
    Checksum: addition of segment contents
    Sender puts checksum value into UDP checksum field

## Slide 8: Connectionless Transport: UDP
UDP Checksum
  Used to detect errors in transmitted segment
  Receiver:
    Compute checksum of received segment
    Check the computed checksum whether it is equal to checksum field value or not
      NO: error detected
      YES: no error detected

## Slide 9: Principles of Reliable Data Transfer
Reliable data transfer is important in applicaiton, transport and link layers
The complexity of reliable data transfer protocol is related to the characteristics of unreliable channel
Incrementally reliable data transfer protocol will be developed.
Only unidirectional data transfer will be considered.

## Slide 10: Principles of Reliable Data Transfer
Rdt 1.0 reliable data transfer over a reliable channel
  No bit errors
  No loss of packets
Rdt 2.0 channel with bit errors
  Channel may flip bits in packet
    Checksum
    Acknowledgements (ACKs)
    Negative Acknowledgements (NAKs)

## Slide 11: Principles of Reliable Data Transfer
Rdt 2.0 channel has a big problem
  What happens if ACK/NAK corrupted? (RDT 2.1 sender handles garbled ACK/NAKs)
  Can not just retransmit: possible duplicate
  Handling duplicates:
    Sender retransmits current paket if ACK/NAK corrupted
    Sender adds sequence number to each paket
    Receiver discards duplicate paket

## Slide 12: Principles of Reliable Data Transfer
Rdt 2.2 NAK-free protocol
  Same functionality as rdt 2.1 using ACKs only
  Instead of NAK receiver sends ACK for last paket received OK
  Duplicate ACK at sender results in same action as NAK: retransmit current paket

## Slide 13: Principles of Reliable Data Transfer
Rdt 3.0 channels with errors and loss
  Underlying channel can also lose packets (data or ACKs)
  Sender waits reasonable amount of time for ACK
  Retransmits if no ACK received in this time
  Requires countdown timer

## Slide 14: Principles of Reliable Data Transfer
Pipelined protocols
  Pipelining: Sender allows multiple in flight yet to be acknowledged pakets
    Range of sequence numbers should be increased
    Buffering
  Two generic forms of pipelined protocols:
    Go-Back-N
    Selective Repeat

## Slide 15: Principles of Reliable Data Transfer
Go-back-N
  Sender can have up to N unacked packets in pipeline
  Receiver only sends cumulative ACKs
  Sender has timer for oldest unacked packet

## Slide 16: Principles of Reliable Data Transfer
Selective Repeat
  Sender can have up to N unacked packets in pipeline
  Receiver sends individual ACK for each packet
  Sender maintains timer for each unacked packet