## Slide 1: COM332
Chapter 3: Transport Layer
(PART 2)

## Slide 2: Outline
Connection-oriented Transport: TCP
Principles of Congestion Control
TCP Congestion Control

## Slide 3: Connection-oriented Transport: TCP
TCP: Overview
  Point-to-point
  Reliable in order byte stream
  Pipelined
  Full duplex data
  Connection-oriented
  Flow-controlled

## Slide 4: Connection-oriented Transport: TCP
TCP round trip time, timeout
  How to set TCP timeout value?
    Longer than RTT
    Too short: Premature timeout, unnecessary retransmissions
    Too long: Slow reaction to segment loss

## Slide 5: Connection-oriented Transport: TCP
TCP creates reliable data transfer service on top of IP’s unreliable service
  Pipelined segments
  Cumulative ACKs
  Single retransmission timer
Retransmission triggered by:
  Timeout events
  Duplicate ACKs

## Slide 6: Connection-oriented Transport: TCP

## Slide 7: Connection-oriented Transport: TCP
TCP fast retransmit
  Time-out period often relatively long
  Detect lost segments via duplicate ACKs
    Sender often sends many segments back to back
    If segment is lost, there will be many duplicate ACKs
  If sender receives 3 ACKs for same data, resend unacked segment with smallest sequence number

## Slide 8: Connection-oriented Transport: TCP
TCP flow control
  Receiver controls sender so sender will not overflow receiver’s buffer
  Receiver advertises free buffer space in TCP header of receiver to sender segments
  Sender limits amount of unacked data to receiver’ free buffer space value
  Guarantees receive buffer will not overflow

## Slide 9: Connection-oriented Transport: TCP
TCP 3-way handshake: FSM

## Slide 10: Principles of Congestion Control
Congestion:
  If too many sources sends too much data too fast for network to handle
  Different from flow control
  Lost packets
  Long delays
  Costs of congestion
    More work retrans) for given goodput
    Unneeded retransmissions

## Slide 11: Principles of Congestion Control
Approaches towards congestion control
  End to end congestion control
    No feedback from network
    Congestion inferred from loss, delay
    TCP uses this approach
  Network assisted congestion control
    Routers provide feedback to end systems

## Slide 12: TCP Congestion Control
TCP congestion control: additive increase, multiplicative decrease
  Sender increases transmission rate until loss occurs
  Additive increase: Increase TCP sender congestion window size by 1 MSS every RTT until loss detected
  Multiplicative decrease: Cut TCP sender congestion window size in half after loss

## Slide 13: TCP Congestion Control
TCP Slow Start
  When connection begins, rate is increased exponentially until first loss event
  Initial rate is slow but ramps up exponentially fast

## Slide 14: TCP Congestion Control
TCP: switching from slow start to CA
  When should the exponential increase switch to linear?
  When TCP sender congestion window size gets to ½ of its value before timeout.

## Slide 15: TCP Congestion Control
TCP fairness
  If K TCP sessions share same bottleneck link of bandwidth R, each should have rate of R/K
  Fairness, parallel TCP connections
    Applicaiton can open multiple parallel connections between two hosts

## Slide 16: TCP Congestion Control
Fairness and UDP
  Multimedia applicaitons often do not use TCP
    Do not want rate throttled by congestion control
  Instead use UDP
    Send audio/video at constant rate, tolerate packet loss