## Slide 1: COM332
Chapter 4: Network Layer
(PART 1)

## Slide 2: Outline
Introduction
Virtual Circuit and Datagram Networks
What is inside a router?

## Slide 3: Introduction
Network layer protocols run in every host and routers
Routers examine header fields in all IP datagrams
Two key network-layer functions
  Forwarding: Move packets from router’s input to matching output
  Routing: Determine route taken by packets from source to dest.

## Slide 4: Introduction
Conncection Setup
  3rd important function in some network architectures
  ATM, frame relay, X.25
  Before datagrams flow, routers establish virtual connection.
  Network layer: between two hosts
  Transport layer: between two processes

## Slide 5: Virtual Circuit and Datagram Networks
Datagram networks provides network-layer connectionless service
Virtual-circuit network provides network-layer connection service
  Service: host-to-host
  No choice
  Implementation: in network core

## Slide 6: Virtual Circuit and Datagram Networks
Virtual Circuits
  Source-to-dest path behaves much like telephone circuit
    Performance-wise
    Network actions
  Each packet carries VC identifier
  Every router on source-dest path maintains state for each passing connection
  Link and router resources may be allocated to VC

## Slide 7: Virtual Circuit and Datagram Networks
Virtual Circuits
  A VC consists of:
    Path from source to destination
    VC numbers one number for each link along path
    Entries in forwarding tables in routers along path

## Slide 8: Virtual Circuit and Datagram Networks
Datagram networks
  No call setup at network layer
  Routers: No state about end-to-end connections
  Packets forwarded using destination host address
  Longest prefix matching:
    When looking for forwarding table entry for given destination address, use longest address prefix that matches destination address

## Slide 9: Virtual Circuit and Datagram Networks
Datagram or VC network
  Internet (datagram)
    Data exchange among computers
    Many link types
    Smart end systems
  ATM (VC)
    Evolved from telephony
    Strict timing, reliability requirements
    Dumb end systems

## Slide 10: What is inside a Router?
Routers has mainly four components
  Router input ports
  Router output ports
  Routing processor
  High-speed switching fabric

## Slide 11: What is inside a Router?
Input port functions
  Physical layer: Bit-level reception
  Data link layer: Ethernet
  Decentralized switching:
    Complete input port processing at line speed
    Lookup output port
    Queuing

## Slide 12: What is inside a Router?
Switching Fabrics
  Move packet from input buffer to output buffer
  Switching Rate: Rate at which packets can be transfer from inputs to outputs
  Three types of switching fabrics
    Memory
    Bus
    Interconnection Network

## Slide 13: What is inside a Router?
Output Ports
  Buffering required from fabric faster rate
    Datagram can be lost because of congestion, lack of buffers
  Scheduling
    Priority scheduling – who gets best performance

## Slide 14: What is inside a Router?
Input port queuing
  Queueing delay and loss due to input buffer overflow
  Head-of-the-Line (HOL) blocking: Queued datagram at front of queue prevents others in queue from moving forward.