## Slide 1: COM332
Chapter 4: Network Layer
(PART 2)

## Slide 2: Outline
IP: Internet Protocol
Routing Algorithms
Routing in the Internet

## Slide 3: IP: Internet Protocol
IP fragmentation
  Network links have MTU largest possible link level frame
  Large IP datagram divided (fragmented) within net
    One datagram becomes several datagrams
    Reassembled only at final destination
    IP header bits used to identify order related fragments

## Slide 4: IP: Internet Protocol
IP address
  32 bit identifier for host, router interface
  Interface is defined as the connection between host/router and physical link
  Routers have many interfaces
  IP addresses associated with each interface

## Slide 5: IP: Internet Protocol
IP address
  Subnet part – high order bits
  Host part – low order bits
  To determine the subnets, detach each interface from its host or router
  Each created isolated network is called a subnet
  CIDR: Classless Inter Domain Routing
    Subnet portion of address of arbitrary length
    Address format: a.b.c.d/x where x is the number of bits in subnet portion of address

## Slide 6: IP: Internet Protocol
DHCP: Dynamic Host Configuration Protocol
  Allow host to dynamically obtain its IP address from network server when it joins network
    Allows reuse of addresses
    Support mobile users
  DHCP overview:
    Host broadcasts DHCP discover
    DHCP server responds with DHCP offer
    Host requests IP address DHCP request
    DHCP server sends address DHCP ack

## Slide 7: IP: Internet Protocol
NAT: Network address translation
  All datagrams leaving local network have same single source NAT IP address, different source port numbers
  Range of addresses not needed from ISP. Just one IP address for all devices
  Addresses of devices in local network can be changed without notifying outside word

## Slide 8: IP: Internet Protocol
NAT: Network address translation
  NAT router must:
    Replace (source IP address port #) of every outgoing datagram to (NAT IP address, new port #)
    Remember every (source IP address port #) to (NAT IP address, new port #) translation pair
    Replace (NAT IP address, new port #) in dest fields of every incoming datagram with (source IP address port #)

## Slide 9: IP: Internet Protocol
ICMP: Internet control message protocol
  Used by hosts & routers to communicate network level information
    Error reporting
      Unreachable host, network, port, protocol
    Echo request/reply
      Used by ping
  Network layer above IP

## Slide 10: IP: Internet Protocol
IPV6
  Initial motivation
    32 bit address space soon to be completely allocated
    Header format may increase speed processing/forwarding
    Facilitate QoS
  IPv6 datagram format
    40-byte header
    No fragmentation

## Slide 11: IP: Internet Protocol
IPV6
  Priority
  Flow label
  Next header
  Checksum
  Options
  ICMPv6

## Slide 12: Routing Algorithms
Routing algorithm classificaiton
  Global or decentralized information
    Global
      All routers have complete topology link cost info
      Link state algorithms
    Decentralized
      Router knows physically connected neighbors link costs to neighbors
      Iterative process of computation
      Exchange of info with neighbors
      Distance vector algorithms

## Slide 13: Routing Algorithms
Routing algorithm classificaiton
  Static or Dynamic
    Static
      Routes change slowly over time
    Dynamic
      Routes change more quickly
        Periodic update
        In response to link cost changes

## Slide 14: Routing Algorithms
A link-state routing algorithm
  Dijkstra’s Algorithm
    Network topology: Link costs known to all nodes
    Computes least cost paths from one node to all other nodes
    Iterative
    Oscillations possible

## Slide 15: Routing Algorithms
Distance vector algorithm
  Bellman-Ford (dynamic programming)
    Key idea: From time-to-time each node sends its own distance vector estimate to neighbors
    Iterative, asynchronous
      Each local iteration caused by: local link cost change or DV update message from neighbor
    Distributed
    Poisoned reverse

## Slide 16: Routing in the Internet
RIP (Routing Information Protocol)
  Included in BSD-UNIX distribution in 1982
  Distance vector algorithm
    Distance metric: Number of hops (max= 15 hops)
    Each link has cost 1
    DVs exchanged with neighbors every 30 sec
    If no advertisement heard after 180 sec, link is declared as dead

## Slide 17: Routing in the Internet
OSPF (Open Shortest Path First)
  Publicly available
  Uses link state algorithm
  OSPF advertisement carries one entry per neighbor
  Advertisements flooded to entire AS