## Slide 1: COM332
Chapter 5: Link Layer
(PART 1)

## Slide 2: Outline
Introduction
Error Detection and Correction
Multiple Access Protocols

## Slide 3: Introduction
Data-link layer transfers datagram from one node to physically adjacent node over a link
Hosts and routers are considered as nodes
Communication channels are considered as links
  Wired links
  Wireless links
  LANs
Layer-2 packet: Frame

## Slide 4: Introduction
Datagrams may be transferred by different link protocols on different links
  Ethernet on first link, 802.11 on last link
Each link protocol provides different services
  May or may not provide reliable data transfer over link

## Slide 5: Introduction
Link layer services
  Framing, link access
  Reliable delivery between adjacent nodes
  Flow control
  Error detection
  Error correction
  Half-duplex and full-duplex

## Slide 6: Error Detection and Correction
Error detection
  Parity checking
    Single bit parity
    Two-dimensional bit parity
  Internet checksum
  Cyclic redundancy check

## Slide 7: Multiple Access Protocols
Two types of links
  Point-to-point
    Between ethernet switch and host
  Broadcast (shared wirw or medium)
    Old-fashioned Ethernet
    Upstream HFC
    802.11 wireless LAN

## Slide 8: Multiple Access Protocols
We have single shared broadcast channel
  Two or more simultaneous transmissions by nodes
    Collision if one of the nodes gets two or more signals at the same time
  Multiple access protocol
    A distributed algorithm that specifies how nodes uses same channel
    Communication about channel sharing must use channel itself

## Slide 9: Multiple Access Protocols
An ideal multiple access protocol
  Broadcast channel of R bps
    When one node wants to transmit, it can send at rate R
    When M nodes want to transmit, each can send at average rate R/M
    Fully decentralized
    Simple

## Slide 10: Multiple Access Protocols
Three broad classes:
  Channel Partitioning
    Divide channel into smaller pieces
  Random access
    Channel not divided, allow collisions
    Recover from collisions
  Taking turns
    Nodes take turns

## Slide 11: Multiple Access Protocols
Channel Partitioning MAC protocols
  TDMA: Time division multiple access
    Access to channel in rounds
    Each station gets fixed length slot
    Unused slots go idle
  FDMA: Frequency division multiple access
    Channel spectrum divided into frequency bands
    Each station assigned fixed frequency band

## Slide 12: Multiple Access Protocols
Random access protocols
  When node has packet to send
    Transmit at full channel data rate R
    No coordination among nodes
  Two or more transmitting nodes creates collision
  Random access MAC protocol defines:
    How to detect collision
    How to recover from collision
  Examples:
    Slotted ALOHA
    ALOHA
    CSMA, CSMA/CD, CSMA/CA

## Slide 13: Multiple Access Protocols
Random access protocols
  Slotted ALOHA
    All frames have same size
    Time divided into equal size slots
    Nodes start to transmit only slot begining
    Nodes are synchronized
    Collision detected by all nodes

## Slide 14: Multiple Access Protocols
Random access protocols
  Pure ALOHA
    Simpler, no synchronization
    When frame first arrives, transmit immediately
    Collision probability increases
    Pure ALOHA efficiency is worse than slotted ALOHA