## Slide 1: COM332
Chapter 5: Link Layer
(PART 2)

## Slide 2: Outline
Multiple Access Protocols (CSMA)
LANs
  Addressing, ARP
  Ethernet
  Switches

## Slide 3: Multiple Access Protocols
Random access protocols
  CSMA (carrier sense multiple access)
    Listen before transmit
    If channel sensed idle transmit entire frame
    If channel sensed busy defer transmission
  Collisions can still take place
    Because of propagation delay, two nodes may not hear each other
    With collision, entire packet transmission time wasted

## Slide 4: Multiple Access Protocols
Random access protocols
  CSMA/CD (Collision Detection)
    Collision detected within sort time
    Transmissions aborted, reducing channel wastage
    Collision Detection
      Easy in wired LANs
      Difficult in wireless LANs

## Slide 5: Multiple Access Protocols
Random access protocols
  Ethernet CSMA/CD algorithm (1)
    1. NIC receives datagram from network layer
    2. Creates frame
    3. If NIC senses channel idle, start transmission. Otherwise waits until channel idle.
    4. If NIC transmits entire frame without detecting another transmission NIC is done

## Slide 6: Multiple Access Protocols
Random access protocols
  Ethernet CSMA/CD algorithm (2)
    5. If NIC detects another transmission while transmitting, aborts and sends jam signal
    6. After aborting, NIC enters binary (exponential) backoff:
      Longer backoff interval with more collisions

## Slide 7: Multiple Access Protocols
Taking turns MAC protocols
  Polling
    Master node invites slave nodes to transmit in turn
    Used with dumb slave devices
    Concerns:
      Polling overhead
      Latency
      Single point of failure

## Slide 8: Multiple Access Protocols
Taking turns MAC protocols
  Token Passing
    Control token is passed from one node to next sequentially
    Token message
    Concerns
      Token overhead
      Latency
      Single point of failure

## Slide 9: LANs – Addressing, ARP
MAC address
  Also called as LAN, Physical or Ethernet address
  48 bit MAC address burned in NIC ROM
  MAC address allocation administered by IEEE
    MAC address: like social security number
    IP address: like postal address
  Portability
    Can move LAN card from one LAN to another
    IP address not portable

## Slide 10: LANs – Addressing, ARP
ARP: Address Resolution Protocol
  Determines interface’s MAC addres knowing its IP address
  Each IP node (host, router) on LAN has ARP table
    IP/MAC address mappings for some LAN nodes
    IP address, MAC address, TTL(Time to live)
  ARP is plug and play

## Slide 11: LANs – Ethernet
Ethernet
  Dominant wired LAN technology
  First widely used LAN technology
  Simple and cheaper
  Kept up with speed race: 10Mbps – 10Gbps

## Slide 12: LANs – Ethernet
Ethernet – Physical topology
  Bus: popular through mid 90s
    All nodes in same collision domain
  Star: prevails today
    Active switch at center
    Each node runs a seperate Ethernet protocol
    Nodes do not collide with each other

## Slide 13: LANs – Ethernet
Ethernet
  Connectionless
    No handshaking between sending and receiving NICs
  Unreliable
    Receiving NIC does not send acks or naks to sending NIC
  Ethernet’s MAC protocol
    Unslotted CSMA/CD with binary backoff

## Slide 14: LANs – Switches
Switches are link layer devices
They store and forward Ethernet frames
Examine incoming frame’s MAC address and selectively forward frame to one or more outgoing links
Transparent
  Hosts are unaware of presence of switches
Plug and play
Self learning
  No need to be configured

## Slide 15: LANs – Switches
Switch: Multiple simultaneous transmissions
  Hosts have dedicated direct connection to switch
  Switches buffer packets
  No collisions, full duplex
  Each switch has a switch table
    Each entry has MAC address of host, interface, time stamp
    Like routing table

## Slide 16: LANs – Switches
Switch: Self learning
  Switch learns which hosts can be reached on which interfaces
    When frame received, switch learns location of sender
    Records sender/location pair in switch table

## Slide 17: LANs – Switches
Switches vs. Routers
  Both are store-and-forward
    Routers are network layer devices
    Switches are link layer devices
  Both have forwarding tables
    Routers compute tables using routing algorithms, IP addresses
    Switches learn forwarding table using flooding, learning, MAC addresses