## Slide 1: CHE138-3
Matrices and Vectors
Matrix and Array Operations

## Slide 2: Matrices and Vectors
Matrix
MATLAB input command
>> A = [2 5 7 8; 5 6 8 3; 1 6 4 0]
2 5 7 8
5 6 8 3
1 6 4 0
2

## Slide 3: Matrices and Vectors
Matrix
MATLAB input command
>> B= [2*x log(x)+sin(y); 5*x 3+2i]
2x ln x + sin y
5x 3 + 2i
3

## Slide 4
4
Special cases: vectors and
scalars
A vector is a special case of a matrix, with just one row or one column
>> u = [1 3 9] produces a row vector
>> v = [1; 3; 9] produces a column vector
A scalar does not need brackets.
>> g = 9.81;
Null Matrix
>> X = [ ]

## Slide 5: Continuation
•
‘...’ usage is not limited to matrix input
5
The following three commands are equivalent
A = [1 3 9; 5 10 15; 0 0 -5];
A = [1 3 9
5 10 15
0 0 -5];
A = [1 3 9; 5 10 ...
15; 0 0 -5];

## Slide 6: Indexing (or Subscripting)
6
» A =[1 2 3; 4 5 6; 7 8 8]
A =
1 | 2 | 3
4 | 5 | 6
7 | 8 | 8
» A(2, 3)
ans =
6
» A(3, 3) = 9 A =
1 | 2 | 3
4 | 5 | 6
7 | 8 | 9

## Slide 7: Indexing (or Subscripting)
7
» B = A(2:3, 1:3)
B =
4 | 5 | 6
7 | 8 | 9
» B = A(2:3, :)
B =
4 | 5 | 6
7 | 8 | 9
» B(:, 2) = []
B =
4 6
7 9

## Slide 8: Dimensioning
No explicit dimension declarations are required
MATLAB creates a matrix just big enough.
If the matrices B and C do not exist already
B(2, 3) = 5; produces
0
5
0 0
0 0
8

## Slide 9: Dimensioning
C(3, 1:3) = [1 2 3]; produces
0
0
2 3
1
0 0
0 0
9

## Slide 10: Dimensioning
10
» C(3, 1:3) = [1 2 3]
C =
0 | 0 | 0
0 | 0 | 0
1 | 2 | 3
» size(C)
ans =
3 3
» [m, n] = size(C) m =
3
n =
3
»

## Slide 11: Matrix Manipulation
the first 10 elements of y.
By specifying vectors as the row and column indices of a matrix one can reference and modify any submatrix.
If A is a 10 X 10 matrix, B is a 5 X 10 matrix, and y is a 20 elements long row vector, then
A([1 3 6 9], :) = [B(1:3, :); y(1: 10)]
replaces 1st, 3rd, and 6th rows of A by the first 3 rows of B, and the 9th row of A by

## Slide 12: Matrix Manipulation
12
Reshaping matrices
  As a vector: All the elements of a matrix A can be strung into a single “column” vector b by the command b = A(:) (A is stacked in vector B).
  As a differently sized matrix: If A is m x n, it can be reshaped into a p x q matrix as long as
m x n = p x q
Thus, for a 6 x 6 matrix A,
>>reshape(A, 9, 4); transforms A into a 9 x 4 matrix,
>>reshape(A, 3, 12); transforms A into a 3 x 12 matrix

## Slide 13: Matrix Manipulation
Transpose of matrix A
– Obtained by typing A’
» A=[2 3; 6 7] A =
2 3
6 7
» B = A' B =
2 6
3 7

## Slide 14: Matrix Manipulation
Transpose example
» u = [0 1 2 3 4 5 6 7 8 9];
» v = u(3:6)'
v = 2
3
4
5

## Slide 15: Initialization
Not necessary but advisable for
Large matrices: (To reserve a continuous block in memory for efficient processing).
>> A = zeros(m, n) % initializes m x n matrix
Dynamix matrices: If the rows or columns of a matrix is computed in a loop you may initialize the matrix to a null mutrix (A = [ ]) and append rows or columns later

## Slide 16: Appending a row or column
» A = [1 0 0; 0 1 0; 0 0 1]
A =
1 | 0 | 0
0 | 1 | 0
0 | 0 | 1
» u = [5 6 7]
u =
5 6 7
» A = [A; u] A =
1 | 0 | 0
0 | 1 | 0
0 | 0 | 1
5 | 6 | 7

## Slide 17: Appending a row or column
0
0
1
4
» A =[1 0 0; 0 1 0; 0 0 1]
A =
1 | 0 | 0
0 | 1 | 0
0 | 0 | 1
» v =[2; 3; 4]
v =
2
3
4
» A = [A v] A =
1 0 0 2
0 1 0 3

## Slide 18: Appending a row or column
18
» A = [1 0 0; 0 1 0; 0 0 1]
A =
1 | 0 | 0
0 | 1 | 0
0 | 0 | 1
» u = [5 6 7]
u =
5 6 7
» A = [A u'] A =
1 | 0 | 0 | 5
0 | 1 | 0 | 6
0 | 0 | 1 | 7

## Slide 19: Appending a row or column
» A = [1 0 0; 0 1 0; 0 0 1]
A =
1 | 0 | 0
0 | 1 | 0
0 | 0 | 1
» u = [5 6 7]
u =
5 6 7
» A = [A u]
??? All matrices on a row in the bracketed expression must have the same number of rows.

## Slide 20: Appending a row or column
» B = []; B = [B; 1 2 3]
B =
1 2 3
» B = []; for k=1:3, B=[B; k k+1 k+2]; end
» B
B =
1 2 3
2 3 4
3 4 5

## Slide 21: Deleting a row or column
Any row(s) or column(s) of a matrix can be de- leted by setting the row or column to null vector
A(2, :) = [ ] deletes the 2nd row of matrix A A(:, 3:5) = [ ] deletes the 3rd through 5th
columns
A([1 3], :) = [ ] deletes the 1st and the 3rd row of A
U(5:length(u)) = [ ] deletes all elements of vector U except 1 through 4

## Slide 22: Utility matrices
eye(m, n)
zeros(m, n)
ones(m, n)
rand(m, n)
returns an m x n matrix with 1’s on the main diagonal
returns an m x n matrix of zeros returns an m x n matrix of ones
returns an m x n matrix of random numbers
Above commands with a single argument, e.g. ones(m), produce square matrices of dimension m

## Slide 23: Utility matrices
generates a diagonal matrix with vector v on the diagonal
extracts the diagonal of matrix A as a vector
extracts the first upper offdiagonal vector of matrix A
diag(v)
diag(A)
diag(A, 1)
A matrix can be built with many block matrices as well.

## Slide 24: Utility matrices
24
» eye(3)
ans =
1 0 0
0 1 0
0 0 1
» B = [ones(3) zeros(3, 2); zeros(2, 3) 4*eye(2)] B =
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 0 | 0
0 | 0 | 0 | 4 | 0
0 | 0 | 0 | 0 | 4
» diag(B)'
ans =
1 1 1 4 4
» diag(B, 1)' ans =
1 1 0 0

## Slide 25: Utility Matrices
» d = [2 4 6 8];
» d1 = [-3 -3 -3];
» d2 = [-1 -1];
» D = diag(d) + diag(d1, 1) + diag(d2, -2)
D =
2 | -3 | 0 | 0
0 | 4 | -3 | 0
-1 | 0 | 6 | -3
0 | -1 | 0 | 8

## Slide 26: Creating Vectors
v = InitialValue:Increment:FinalValue
(If no increment is specified, increment is 1)
a = 0:10:100
u = 2:10
produces a = [0 10 20 ... 100],
produces a = [2 3 4 ... 10]
No square brackets are required above.
However, to force concatenation you need them
– u = [1:10 33:-2:19]

## Slide 27: Creating Vectors
linspace(a, b, n) generates a linearly spaced vector of length n from a to b.
logspace(a, b, n) generates a logarithmically spaced vector of length n from 10a to 10b.
u = zeros(1, 1000) initializes a 1000 element long row vector
v = ones(10, 1) creates a 10 element long column vector of 1’s.
» u = linspace(0, 20, 5) u =
0 5 10 15 20
» v = logspace(0, 3, 4) v =
1
10
100
1000

## Slide 28: Matrix and Array Operations
is valid if A and B are of the same size
is valid if A’s number of columns equals B’s number of rows
is valid, and equals A.B-1 for same size square matrices A & B
makes sense only if A is square and equals A*A
A+B or A-B
A*B
A/B
A^2

## Slide 29: Matrix and Array Operations
In all the previous comands if B is replaced by a scalar, say w, the arithmetic operations are still carried out. A+w adds w to each element of A, w*A (or A*w) multiplies each element of by w and so on.
The right division: This division is used to solve a matrix equation. In particular,
X = A\b solves the matrix equation A x = b.

## Slide 30: Matrix and Array Operations
Element-by-element multiplication, division and exponentiation between two matrices or vectors of the same size are done by preceding the corresponding arithmetic operators by a period (.):
.*
./
.\
.^
.’
element-by-element multiplication element-by-element left-division element-by-element right-division element-by-element exponentiation nonconjugated transpose

## Slide 31
Matrix and Array Operations
» A=[1 2 3; 4 5 6; 7 8 9];
» x = A(1, :)'
x =
1
2
3
» x'*x ans =
14
» x*x' ans =
1 2 3
2 4 6
3 6 9
» A*x ans =
14
32
50

## Slide 32: Matrix and Array Operations
» v = [ 1 2 3 4 5 6]
v =
1 2 3 4 5 6
» 1./v ans =
1.0000 0.5000 0.3333 0.2500 0.2000
0.1667

## Slide 33: Matrix and Array Operations
33
There is a big difference between A^2 and A.^2
» A = [1 2 3; 4 5 6; 7 8 9]
A =
1 | 2 | 3
4 | 5 | 6
7 | 8 | 9
» A^2 |  | 
ans = |  | 
30 | 36 | 42
66 | 81 | 96
102 | 126 | 150
» A.^2 |  | 
ans = |  | 
49
1 | 4 | 9
16 | 25 | 36
 | 64 | 81

## Slide 34: Matrix and Array Operations
Relational Operations
<
<=
>
>=
==
~=
less than
less than or equal greater than
greater than or equal equal
not equal
These operations result in a vector or matrix of the same size as the operands, with 1 where the relation is true and 0 where false.

## Slide 35: Matrix and Array Operations
Relational operations
» x = [1 5 3 7];
» y = [0 2 8 7];
» k = x <= y k =
0 0 1 1
» k = x >= y k =
1 1 0 1
» k = x ~= y k =
1 1 1 0

## Slide 36: Matrix and Array Operations
Logical operations
&
|
~ xor
logical AND logical OR
logical complement (NOT) exclusive OR

## Slide 37: Matrix and Array Operations
» x = [0 5 3 7];
» y = [0 2 8 7];
» m = (x>y)&(x>4)
m =
0 1 0 0
» n = x|y n =
0 1 1 1
» m = ~(x|y) m =
1 0 0 0
» p = xor(x, y) p =
0 0 0 0

## Slide 38: Matrix and Array Operations
Built-in logical functions
all
any
exist
– isempty
true (=1) if all elements of a vector are true true (=1) if any element of a vector is true true (=1) if the argument (a variable or
function) exists
true(=1) for an empty matrix
isinf true for all infinite elements of a matrix
isfinite true for all finite elements of a matrix
isnan true for all elements of a matrix that are
Not-A-Number
find finds indices of non-zero elements of a matrix

## Slide 39: Matrix and Array Operations
» x = [7 -2 9 -1 -3 10];
» all(x<0)
ans =
0
» A = [1 inf; 2 3];
» isfinite(A)
ans =
1 0
1 1
» x = [0 2 5 7];
» find(x)
ans =
2 3 4
» i = find(x>5) i =
4

## Slide 40: Matrix and Array Operations
Matrix functions
finds the exponential of matrix A, eA finds log(A) such that A = e log(A)
expm(A)
logm(A)
sqrtm(A)
finds A
Array Counterparts that operate on each element of the input matrix
  exp
  log
  sqrt

## Slide 41
41
» A = [1 2; 3 4];
» asqrt = sqrt(A)
asqrt =
1.0000 1.4142
1.7321 2.0000
» Asqrt = sqrtm(A)
% Thus [Asqrt]*[Asqrt]=[A]
Asqrt =
0.5537+ 0.4644i
1.2104- 0.3186i
0.8070- 0.2124i
1.7641+ 0.1458i
» exp_aij = exp(A)
exp_aij =
2.7183 7.3891
20.0855 54.5982
» exp_A = expm(A)
% Finds the true matrix exponential eA
exp_A =
51.9690 74.7366
2005112.1048 164.0738
Matrix and Array Operations

## Slide 42
Character Strings
>> message = ‘Leave me alone’ creates a vector of size 1 x 14
  To create a column vector of text objects, each text string must have exactly the same number of characters
>> names = [‘John’; ‘Ravi’; ‘Mary’; ‘Xiao’]
  Thus
>> A = [‘Ali’; ‘Veli’]
generates an error
Character strings

## Slide 43
Character Strings
  ‘char’ command pads the necessary spaces
>> howdy = char(‘Hi’, ‘Hello’, ‘Namaste’) is valid.
  Character strings can be manipulated just like matrices.
>> c = [howdy(2,:) names(3,:)] produces Hello Mary as the output in variable c.
Matrix and Array Operations

## Slide 44
Charater Strings
  ‘eval’ function evaluates text strings and execute them if they contain valid commands
    eval(‘x = 5*sin(pi/3)’) is equivalent to x = 5*sin(pi/3)
    You make ‘eval’ useful by using variables in the string.
Matrix and Array Operations