## Slide 1: 55490005
Chapter 1: Introduction (PART 1)

## Slide 2: Outline
What is the Internet?
Network Edge
Network Core

## Slide 3: What is the Internet?
Internet can be considered as network of networks
There are millions of connected devices in the Internet.
Those devices can be named as end systems or hosts.
They run network applicaitons.
There are many types of communicaiton links.
  Fiber, copper, radio, satellite
  All have different transmission rates.

## Slide 4: What is the Internet?
One of important concepts of Internet is packet switches
They forward packets coming from one input interface to a specified output interface.
There are actually two types of packet switches
  Routers
  Switches
Another valuable concept here is protocols.
They define and control packet sending and receiving process

## Slide 5: What is the Internet?
Internet can also be defined as an infrastructure that provides services to network applications
Network applications have a broad range: Web, VoIP, email, games, e-commerce, social networks ...
Internet provids programming interface to network applicaitons.

## Slide 6: What is the Internet?
There are many network protocols in Internet.
Protocols define the rules of communicaiton with respect to format, order of messages sent and received among end systems.
They also specify the actions to be taken whenever a new message receipt.

## Slide 7: Network Edge
End systems, access networks and communication links are considered as network edge.
End systems (be also called as hosts) can be clients or servers.
Communication links can be wired or wireless.

## Slide 8: Network Edge
Access networks are used to connect hosts to edge router.
  Residential access networks
  Institutional access networks (school, company)
  Mobile access networks
There are two concepts in access networks
  Bandwidth (bits per second)
  Shared or dedicated

## Slide 9: Network Edge
Hosts send packets of data to receiver.
Application message is broken into smaller pieces known as packets.
The length of packets is L bits.
The link transmission rate is R.
The packet transmission delay that is the time needed to transmit L bits into link is computed as follows:
L (bits) / R(bits/sec)

## Slide 10: Network Core
Network core can be considered as a mesh of interconnected routers.
Sending host breaks applicaiton layer data into packets.
Those packets are transmitted. On network core, each packet is forwarded from one router to the next one based on the path (packet switching).
The full link capacity is used for individual link capacity.

## Slide 11: Network Core
Store and Forward
  All the bits in a packet must be arrived at a router in order to be transmitted to next link.
  It takes L / R seconds to push out all the bits of L-bit packet into link at R bps.
  Example: L =7.5 Mbits R=1.5 Mbps
  One hoop tranmission delay is 5 seconds.

## Slide 12: Network Core
Queueing delay, loss
  If the arrival rate of packets in a router much more than the transmission rate of link for a while, packets will need to be placed in a queue in buffer.
  They need to wait to be transmitted.
  If buffer fills up, some of the coming packets may be dropped.

## Slide 13: Network Core
There are two key functions in network-core
  Routing
  Forwarding
Routing is the process of finding the path between source and destination using routing algorithms.
Forwarding is the process of moving packets from one input interface to one output interface.

## Slide 14: Network Core
Circuit switching is another approach for network core.
End to end resources are reserved for the communicaiton between source and destination.
With this approach, there is guaranteed performance with dedicated resources.
Used in traditional telephone networks.

## Slide 15: Network Core
Packet switching vs circuit switching
  Packet switching allows more users to use network.
  It is great for bursty data.
  Call setup is not needed.
  Packet delay and packet loss may take place therefore we need reliable data transfer protocols.