## Slide 1: 55490005
Chapter 1: Introduction
(PART 2)

## Slide 2: Outline
Delay, loss, throughput in networks
Protocol layers, service models
Security

## Slide 3: Delay, Loss, Throughput in Networks
If the packet arrival rate at router exceeds output link transmission rate, packets are stored at buffer. Queueing delay takes place.
If there are no free buffers, packets dropped (loss) and need to be resend using reliable data transfer protocols.

## Slide 4: Delay, Loss, Throughput in Networks
Actually there are four types of delays
dp= nodal processing delay
  The delay for checking bit errors and determining output link
  Normally it is less than msec.
dq= queueing delay
  The delay for waiting at output link for transmission
  This delay depends on the level of congection at router.

## Slide 5: Delay, Loss, Throughput in Networks
Actually there are four types of delays
dt= transmission delay
  To transmit all the bits into the link
  dt= L / R (bits / bitsps)
dp= propagation delay
  The delay on which packets are on the link.
  d: length of physical link
  s: propagation speed in medium (~2 x 108 m/sec)
  dp= d /s

## Slide 6: Delay, Loss, Throughput in Networks
Caravan Analogy
We have 10 car caravan. Cars propagates at 100 km/hour. Toll booth takes 12 sec to service a car.
We may consider car as bit and caravan as packet.
How long it takes the caravan is lined in front of second toll booth?
Answer: 62 min.

## Slide 7: Delay, Loss, Throughput in Networks
Queueing Delay
R: link transmission rate
L: packet length in bits
a: average packet arrival rate
La/R ~ 0 : average queueing delay is small
La/R = 1 : average queueing delay large
La/R >1 : average delay infinite

## Slide 8: Delay, Loss, Throughput in Networks
traceroute
  It provides delay measurement from source to each router that is on the path to destination.
  It send three packets.
  Each router will return packets to sender.

## Slide 9: Delay, Loss, Throughput in Networks
Throughput
  The actual rate (bits/time) at which bits transferred between sender and receiver.
  There are two types of throughput:
    instantaneous (rate at a specific point in timeline)
    average (rate over longer period of time)

## Slide 10: Protocol Layers, Service Models
So far, we discussed many concepts like hosts, routers, links, applications and protocols.
We need an organizing structure of network.
We need to deal with complex network system.
Layering is used to identify the relationship of complex systems’ pieces
It also provide modularizaiton that makes maintenance and updating of system easier.
The modifications on one layer should not affect the functionality on other layers.

## Slide 11: Protocol Layers, Service Models
Internet Protocol Stack
  Application Layer
    FTP, SMTP, HTTP
  Transport Layer
    TCP, UDP
  Network Layer
    IP, routing protocols
  Data Link Layer
    Ethernet, 802.111, PPP
  Physical Layer
    Bits on the wire

## Slide 12: Protocol Layers, Service Models
ISO/OSI Reference Model
  Application
  Presentation
  Session
  Transport
  Network
  Link
  Physical

## Slide 13: Network Security
Network Security
  Bad guys can attack computer networks
  How we can defend networks against attacks
  How we can design architectures

## Slide 14: Network Security
Network Security
  Malware can get in host from
    Virus: Self-replicating infection. Executing object is mandatory.
    Worm: Self-replicating infection. Passively receiving object is sufficient.
  Spyware malware can record keystrokes, web sites visited.
  Infected host can be enrolled in botnet. Used for DDoS attacks.

## Slide 15: Network Security
Network Security
  Denial of Service (DoS): Using bogus traffic, resources are made unavailable.
    Selection of target
    Breaking into hosts around the network
    Sending packets to target from compromised hosts

## Slide 16: Network Security
Network Security
  Packet Sniffing
    Packet sniffer reads/records all packets passing by.
  IP Spoofing
    Sending packets with false source address.